## Slide 1: DRM Support for off-catalog systems
Geoff Dillon, Sebi Paul
9/24/2018
Internal Use - Confidential

## Slide 2: Current vs Proposed Update Delivery
Current
New firmware Updates for DCS1610/ DSS9600 are tested by ESI with customer config.
ESI Support team delivers Updates by request, individually.
Customer updates systems ad-hoc. (Possibly one-by-one, not sure of process.)
Proposed
New firmware Updates are tested by ESI.
ESI Support team imports new updates into Dell Repository Manager repositories targeted for DCS1610/ DSS9600.
Team exports the repository and zips the resulting files for delivery to the customer.
Customer unzips files to a file share (NFS/Windows/TFTP/…)
Customer systems auto-update via iDrac Automatic Updates, scheduled, en masse.
Value Added: Easier update distribution for hundreds of systems.

## Slide 3: Dell EMC Repository Manager Typical Use
Dell.com
DRM
Target system repo
PE systems
Download CatalogsDUPs
Target system DUPs
File share
ISO
PE systems
PE systems
PE systems
PE systems
PE systems
PE systems
PE systems
iDrac Auto Update
Export
Manual boot
Client PC
Update systems
Assemble Repository

## Slide 4: Dell EMC Repository Manager Typical Use
Two phases: Assemble Repository and Update Systems
Maintains repositories of Dell firmware updates for PE systems
For PowerEdge Systems with full eSupport
Client PC - Download/install DRM
Download Updated Enterprise catalog or index catalogs
Create repositories for target systems from catalog
Download DUP’s from dell.com into repository
Export update media (ISO) or file share from repository
Monthly update catalog and DUPs from downloads

## Slide 5: DRM limitations with DCS1610
DCS1610 system is not enabled for eSupport
  Not intended for general sales, only specific customers. (eSupport is public)
System is not listed in the public catalogs
  If DRM can’t identify system ID, the it can’t make a repository
Not all firmware is available for download
  Available - Common PE DUPs (Disks, RAID)
  Not available - System-specific DUPs (BIOS, iDrac, PSU, CPLD)
  These items must be delivered by support directly.

## Slide 6: DRM limitations with DSS9600
DSS9600 system is enabled for eSupport
System is not currently listed in the Enterprise base catalog
  DSS systems are not supported by Enterprise catalog team.
Most firmware appears to be available from eSupport. (support.dell.com)
Base Catalog Updates with custom catalog not very helpful
  Would have to make new repository every time rather than just update existing.
  Easier to manually update repository and export files.

## Slide 7: DRM Custom Catalog Use Case
Dell.com
DRM
Target system repo
DCS1610
Download Common DUPs
Target system DUPs
File share
ISO
iDrac Auto Update
Export
Manual boot
Client PC
Custom Catalog
Add
Import
New version DUPs
Extra DUPs
File transfer
DCS1610
DCS1610
DCS1610
DCS1610
DCS1610
DCS/DSS
DCS
(Customer)
Update systems
(Dell)
Assemble Repository
ESI Support

## Slide 8: DRM delivery with DCS/DSS systems
What can we do?
  Empower customer to update hundreds of systems with minimum effort.
  Provide updates as needed, or on a schedule.
Deliver updates packaged for iDrac Automatic Updates consumption
  Maintain DRM repository here and export updates as needed.
Updates to repository
  Delivered directly by CST as complete set with built-in xml.
  Customer replaces old files with new
  Systems pick up updates on schedule.